## Slide 1
Environmental Assessment of Road Transport in Qatar and its policy implications:
Current Emissions and Projections for Future Reductions
Abdulla Alishaq
Supervisor: Jeremy Woods

## Slide 2
Background: GHG and Air Pollution | 
The Transport Sector | 
Research Aim | 
Research Methods | 
Initial Results | 
Conclusion and Future Work | 
Reference | 
Presentation Outline

## Slide 3: Background: GHG and Air Pollution
Highest CO2 per capita
31.1 tonnes vs 4.8 tonnes
Heavily involved in oil and gas business
Hydrocarbons accounted for 91% of exports
126 million tonnes of LNG production by 2027
12th most polluted city
PM2.5
WHO Standard: 10 μg/m^3
Qatar: 90 μg/m^3
PM10
WHO Standard: 20 μg/m^3
Qatar: 50 μg/m^3
01
02
03

## Slide 4: The Transport Sector
GHG emissions
7.67/12 mega tons of CO2eq in 2019
7% of national emissions
8.5 billion tonnes of CO2eq in 2019
Road vehicles are responsible for 45%
50% of PM emissions in OECD
1.5 million road vehicles
300,000 vehicles in 2000
800,000 vehicles in 2010
1.5 million vehicles in 2018
Targets
Electricity 4% of road fleet by 2022
Electricity 10% of road fleet by 2030
Reduce road emissions by 25% by 2030

## Slide 5: Research Aim
The aim of this research is to determine which policies should Qatar adopt for road transport this decade to put it on track to achieve 2030 and 2050 goals.
What fleet configuration of would achieve the GHG reduction goals by 2030 and how would vehicle ban scenarios affect emissions?
What are the necessary measures to decarbonize the transportation sector in Qatar by 2050?
What is the dynamic LCA from cradle to grave of a BEV in comparison to an ICEV operating in Qatar?
Research questions:

## Slide 6: Methodology
Scenarios analysis for road transport
1- Current GHG and air pollution emissions?
2- How to get a 25% reduction?
3- Impact of 10% electrification by 2030?
4- Impact of ICEV ban?
Stock Flow Model
Inflow and outflow of vehicles
LDV, HDV, buses, and motorcycles
LDV: sedans, SUV, and sports vehicles
Survival and scrappage rate
Fuel source
Fuel economy
Vehicle kilometres travelled
Curb mass

## Slide 7: Methodology
Scenarios analysis for road transport
Average transport activity per person per mode (pkm/person)
Population
Total average transport activity per mode (pkm)
Vehicle transport distance per mode (vkm)
Vehicle transport distance per mode per technology (vkm)
Technology Share (%)
Occupancy rate (pkm/vkm)
Total GHG emissions (kgCO2eq)
Emission factor per mode per technology (kgCO2eq/MJ)
Energy intensity per mode per technology (MJ/vkm)

## Slide 8: Methodology
Emission projections using the transition pathway explorer

## Slide 9: Methodology
Emission projections using the transition pathway explorer

## Slide 10: Methodology
Life Cycle Assessment
LDV+ HDV+ Buses
LDV: Sedans, SUV, Sports Vehicles
BEV + ICEV + Diesel
Life Cycle Assessment
Dynamic Life Cycle Assessment
Literature | Powertrain | Type of LDV | Impact Assessment Method | Database | Boundary
Al-Thawadi, Weldu and Al-Ghamdi | ICEV | Not Specified | TRACI | GaBi Database | Gate to Gate
Al-Thawadi and Al-Ghamdi | ICEV | Not Specified | ReCiPe | GaBi Database | Gate to Gate
Onat, Kucukvar, Aboushaqrah, and Jabbar | ICEV, HEV, PHEV, BEV | SUV | Multi-Region Input-Output | EXIOBASE 3.4 | Gate to Gate
This Study | ICEV and BEV | Sedans, SUVs, and Sports Cars | CML | Ecoinvent | Cradle to Grave

## Slide 11: Initial Results
Scenarios analysis for road transport
Chart: Total CO2 Emissions from All Road Vehicles
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
LDV | 5849870.4554 | 6393911.5194 | 6831656.3938 | 7001970.5888 | 7474164.8552 | 7362785.9665 | 6719420.0695 | 7133916.5376 | 7383505.9391 | 7533603.1011 | 7710306.5385 | 7860005.7423 | 8054443.0085 | 8295938.6977 | 8543716.5317 | 8798559.1253 | 9059977.7986
HDV | 1090692.46 | 1240959.3529 | 1340926.7932 | 1365249.0826 | 1470986.8065 | 1419197.9856 | 1291030.9085 | 1376942.0061 | 1422598.7658 | 1448372.7548 | 1479623.7692 | 1509776.5032 | 1547014.2038 | 1593767.8768 | 1641782.753 | 1691133.3831 | 1741958.5254
Buses | 50301.9959 | 59783.225 | 60340.9444 | 60512.5503 | 60662.7056 | 63821.4804 | 61349.2793 | 61910.9385 | 63963.2232 | 65134.4289 | 66539.9163 | 67890.4643 | 69553.0281 | 71667.1567 | 73817.0158 | 76045.3815 | 78335.8119
Motorcycles | 5516.9208 | 6467.4784 | 7231.1921 | 8270.5634 | 9623.7151 | 8140.7416 | 7398.6366 | 7901.7311 | 8159.4967 | 8302.0028 | 8478.5136 | 8652.4689 | 8866.464 | 9134.036 | 9409.9069 | 9693.6346 | 9986.0634
Chart: CO2 Emissions from LDVs
| 2014 | 2015 | 2016 | 2017 | 2018
Sedans | 2280398.6323 | 2492475.7682 | 2663120.9645 | 2775211.6017 | 2913581.9023
SUVs | 2420499.4071 | 2645609.7829 | 2826732.1465 | 2828476.5454 | 3092581.6699
Sports Vehicles | 1148972.4159 | 1255825.9683 | 1341803.2827 | 1398282.4417 | 1468001.2829

## Slide 12: Initial Results
Life Cycle Assessment
Chart: 
| ICEV Sedan | ICEV SUV | ICEV Sport Vehicle | BEV Sedan | BEV SUV | BEV Sport Vehicle
Global Warming (GWP100a) | 0.20858 | 0.36497 | 0.22954 | 0.12745 | 0.15582 | 0.16798
Chart: 
| ICEV Sedan | ICEV SUV | ICEV Sport Vehicle | BEV Sedan | BEV SUV | BEV Sport Vehicle
Eutrophication | 0.00015633 | 0.00033684 | 0.0001616 | 0.00053252 | 0.0007753 | 0.00066102

## Slide 13: Conclusion and Future Work
Develop road scenarios to achieve local goals, and measure the effectiveness of ban policies
01
Begin working on the transition pathway explorer model
02
Model the dynamic LCA for different vehicle types and classes
03

## Slide 14: References
Al-Thawadi, F. E., & Al-Ghamdi, S. G. (2019). Evaluation of sustainable urban mobility using comparative environmental life cycle assessment: A case study of Qatar. Transportation Research Interdisciplinary Perspectives, 1(2019), 100003.
Al-Thawadi, F. E., Weldu, Y. W., & Al-Ghamdi, S. G. (2020). Sustainable Urban Transportation Approaches: Life-Cycle Assessment Perspective of Passenger Transport Modes in Qatar. Transportation Research Procedia, 48, 2056–2062.
Onat, N. C., Kucukvar, M., Aboushaqrah, N. N. M., & Jabbar, R. (2019). How sustainable is electric mobility? A comprehensive sustainability assessment approach for the case of Qatar. Applied Energy, 250, 461–477.
Qatargas. (2020b). Retrieved December 1, 2020, from https://www.qatargas.com/english/MediaCenter/Pages/Press Releases/Qatar-Petroleum-Announce-the-Start-of-the-Development-Drilling-Campaign-of-the-North-Field-East-Project.aspx
Garcia, R., & Freire, F. (2017). A review of fleet-based life-cycle approaches focusing on energy and environmental impacts of vehicles. Renewable and Sustainable Energy Reviews, 79(August 2016), 935–945.
Taylor, E., Martin, B., Latiers, M., Cornet, M., & Pestiaux, J. (2020). Transport Module Documentation.
eucalc. (n.d.). Retrieved June 20, 2022, from http://tool.european-calculator.eu/app/emissions/ghg-emissions/?levers=1j12112ffl11211mp2b111fffffpppppp11f411111e3211r211l21n221
Ministry of Interior. (2019). TRANSPORT AND COMMUNICATIONS STATISTICS.
1
5
2
6
3
7
4
8

## Slide 15
Thank you